## Slide 1: Cross-Bores – Best Practices Outreach and Education
Jim Marean
Gas Technology Institute
Notes: Thank you for the opportunity to present this information on cross bore best practices.
The presentation will be focused on improving safety for both existing installation where a cross bore may have occurred as well as for new installations to ensure no new cross bores occur
We will review:
  What cross bores are
  How they occur
  Why you should care
  What we did to develop the best practices guide
  What’s included in the guide

## Slide 2: Jim Marean – Senior Program Manager
Senior Program Manager, Intelligent Infrastructure Initiative
As a Senior Program Manager for GTI’s intelligent infrastructure initiative, Jim Marean leads efforts to assess and articulate natural gas’ role and value as part of the smart energy grid. In 2011 Jim co-authored a white paper (available on the GTI website) with Navigant Consulting titled Natural Gas in a Smart Energy Future which provides a compelling vision for the natural gas industry through 2030 and beyond.
Marean comes to GTI from New York State Electric and Gas (NYSEG), where he spent 30 years in positions of increasing responsibility. His background includes a variety of management and technical research responsibilities. He has wide-ranging experience with distribution engineering, natural gas and compressed air energy storage evaluation, alternative fuel and natural gas vehicles, environmental matters and manufactured gas plant investigation and remediation strategies.
Most recently at NYSEG he managed a large technical support services team, with significant focus on new innovations in technology and demonstration deployment. He has specific expertise in smart energy grid technology, geographic information systems and data mapping, bio-methane to pipeline quality, and exploration of new energy sources like wind and solar technologies.
He has held positions on the Board of Directors for Operations Technology Development (OTD) and Utilization Technology Development (UTD). Marean earned a B.S. degree in Wildlife Biology and an M.S. in Fisheries Biology from SUNY Environmental Science & Forestry, and an M.S. in Science Education from Syracuse University.

## Slide 3: Cross Bore Program
Cross Bore Best Practices Guide - single source of information for natural gas operators to investigate and remediate existing cross bores as well as prevent future cross bores
Outreach and Education Program - information to effect positive changes in attitude, practices and operations.
Cross Bore Database - A national database of damages and incidents to assist in identifying trends.
New Developments – Acoustic Pipe Locator, Cross Bore Detection, Obstacle Detection
Notes: Best Practices Guide
OTD Project 1.11.d, GTI Project 21178
Issued January, 2011
The development of this Guide included the review of information from a wide variety of sources across North American (excluding Mexico) including numerous natural gas distribution companies that were either individual companies or multiple companies as part of a larger holding company referred to here as Local Distribution Companies (LDCs), installation contractors, remediation contractors, equipment providers, industry associations and industry literature. The combined customer base of the 23 LDCs interviewed represent 80% of the 75 million natural gas customers in the United States and Canada. The information included in this Guide summarizes the best practices to investigate and remediate existing cross bores and to avoid future cross bores during the process of installing new mains and services. Specific conversations and company specific documents have been kept confidential unless the information is in the public domain or a release has been provided by the company. 84 Pages
Outreach & Education Program – Phase 2 of OTD/GTI Best Practices Projects
To develop an outreach program to raise awareness and streamline implementation of cross bore best practices with natural gas system operators, other utility operators, the sewer and plumbing industry and the contractor community at large. This program will provide information to effect positive changes in attitudes, practices and operations related to cross bores.
Cross Bore Database
OTD Project 1.11.e, GTI Project 21186 Ongoing
To develop a national database to address the cross bore issue in the natural gas industry. The national database will collect information from natural gas operators on damages and incidents to assist in identifying trends and gaining a better understanding of the scope of the cross bore threat.

## Slide 4: Table of Contents
Introduction to Cross Bore
Regulatory Reactions
Best Practices
  Tidbits and Observations
  Quick Guide
  Who to Involve
  Public Awareness
  Tailgate Briefings
  Documentation
New Developments

## Slide 5: Introduction to Cross Bores
http://www.youtube.com/watch?v=g_dUMLSLYtw&feature=email or Library
Notes: The showing of an informational video of a newscast of a cross bore incident in St Paul, MN in 2010. The video shows:
The severity of an incident when a cross bore is mis-handled;
The uninformed efforts of the homeowner to clear the clog that could have resulted in the catastrophe that ultimately occurred;
The efforts of a plumber who did not recognize the clog as a potential cross bore and used a cleaning tool, severing the gas pipe resulting in the catastrophe and
The emergency response from various organizations. A link to the video is provided on the OTD website;

## Slide 6: Cross Bores – What are They and Why is There Concern?
What is a sewer cross-bore? A sewer cross-bore is the inadvertent placement of a gas main or service through a sewer line. Cross-bores typically occur during trenchless construction. What can happen? A blockage may occur.
Clearing the line may damage the gas line which could result in an explosion or fire.
Notes: The terms sewer or sewer system are used exclusively throughout this Guide to represent both the sanitary and storm sewer systems, as well as private septic systems.

## Slide 7: Types of Cross Bores
Legacy Cross Bores
Cross bore events that currently exist due to previous installations.
Investigate using a risk-based approach that progresses from a review of records to a focused field investigation
Future Cross Bores
Cross bores that do not currently exist but may occur as new gas mains and services are installed.
Notes: Items to Consider:
First date when trenchless technology was used to install mains or services
Do not assume that the lack of a natural gas services installation excludes a location

## Slide 8
Notes: This is one scenario representing possible cross bore locations

## Slide 9: Regulatory Reactions
First Incident – Kenosha, WI 1976
Investigations
Minnesota Department of Public Safety Alert

## Slide 10: First Recorded Cross Bore Incident Kenosha, WI August 29, 1976
NTSB Recommendations
Complete inspection of those locations along the construction route where gas mains and sewer laterals may be in proximity to one another and correct any deficiencies.
Examine records to determine other locations where gas lines were installed near existing sewer facilities (including a review of sewer blockage complaints), then inspect these locations and take corrective action where necessary.
Revise construction standards to require the underground facilities be located accurately before construction and to provide protection for these facilities near boring operations.
Inform inspectors and supervisory personnel of the circumstances of this accident, train them to be alert for similar conditions, and advise them of preventive actions.
Notes: NOTE:
2 deaths, 4 injuries
The first recorded event was at a location that was not a natural gas customer
The first recorded event was in 1976, over 36 years ago
The full text of the NTSB recommendations can be found in Appendix A of the Guide.
Or by going to the following - National Transportation Safety Board, Safety Recommendation(s), Pg. 76-83 through 76-86, Issued November 12, 1976. http://www.ntsb.gov/recs/letters/1976/P76_83_86.pdf

## Slide 11: Cross Bore Investigative Results
Minnesota Public Utilities Commission - 27 cross bores reported in a 6 month period
Palo Alto, CA - 4 blocks inspected. 24 cross bores found
City A - 2 cross bores per mile in 200 miles of sewer main, One cross bore at a school
City B - 3 cross bores per mile of sewer main, One cross bore at a hospital
City C - 2% cross bores out of 11,000 sewer laterals inspected
Cross Safety Association – 2-3/mile of sewer main
Notes: It was noted during the surveying of companies that when a cross bore is reported it is probable that others may have occurred in the same are due to similar utility installation practices or field conditions

## Slide 12: Minnesota Department of Public Safety – Alert Notice May 10, 2010
Aware of at least 155 instances believes there are more
Inadvertently installed due to trenchless construction techniques
The majority were found by plumbers while cleaning sewer service laterals
Since 2000, six gas lines have been punctured by sewer cleaning contractors three ignited
Notes: https://dps.mn.gov/divisions/ops/forms-documents/Documents/Alert%20Notice%2001-2010.pdf
Use the link shown above for more information.

## Slide 13: Best Practices
Tidbits and Observations
Quick Guide
Who to Involve

## Slide 14: OTD Project Cross Bore Best Practices
Sources – LDCs, Installation and Remediation Contractors, Equipment Providers, Industry Associations and Industry Literature http://www.otd-co.org/Documents/OTD_1_11_d_FinalReport_Nov2012_PublicVersion.pdf
Guide provides information that can be used to investigate and remediate existing cross bores as well as prevent future cross bores.
Notes: The combined customer base of the 23 LDCs interviewed represent 80% of the 75 million natural gas customers in the United States and Canada.
The first section of the Guide provides best practices and general guidelines for LDCs on the cross bore topic.
The second section of the Guide provides best practices for addressing cross bore events that currently exist due to previous installations, referred to in the Guide as legacy installations or legacy cross bores.
The third section of the Guide is focused on preventing cross bores during new installations.
The Guide also provides contact information for organizations with additional information and a series of appendices that provide the full text of the NTSB summary of the first incident investigation in 1976, examples of a wide variety of communications and education materials, a summary of cross bore related legislation and regulations and a summary of technologies under evaluation for further development to detect if a transaction of a sewer line has taken place as part of a new installation.

## Slide 15: Tidbits and Observations (1)
Interviewed 23 LDC’s
  Regional Differences in the Approach Used to Assess
    Likelihood of a full basement or the need to construct the sewer at a depth to be below the level of frost penetration
    Soil conditions
    The influence of existing or proposed legislation
    The use of the One-Call System or Call Before You Clear programs
    The use of bi-lingual outreach materials
    A "found" cross bore was the best indicator that there may be others in the immediate area

## Slide 16: Tidbits and Observations (2)
Legacy Program Status – of 23 Companies
  9 (~39%) have a legacy program in place
  4 (~17%) are developing a legacy program
  3 (~13%) do not have a legacy program but are exploring the option
  7 (~30%) do not have a legacy program
Legacy Program - Change in Process
  4 of 23 companies made a process change that facilitates inspection or discovery of legacy cross bores
  Most Beneficial Changes
    Collaborative effort with the sewer operators
    Separate department or an integrated team with a common goal, focus, and awareness
Notes: The terms sewer or sewer system are used exclusively throughout this Guide to represent both the sanitary and storm sewer systems, as well as private septic systems.

## Slide 17: Best Practices – Quick Guide
Dedicated Resources
Lack of Natural Gas Service Does Not Excludes a Location
Auditable Record Keeping System
Organizational Commitment
Operating Procedures and Training Specific to Cross Bores
Support From Highest Level
Compliance with All Regulations
Risk Based Approach
Use a GIS
Common Goals
Coordinate With One Call Systems
Customer Type
Previous Claims or Incident Reports
Attributes with Higher Probability
Include in DIMP
Notes: Risk Based Approach
A cross bore to a sewer serving a home or business can occur regardless of whether the structure is served by natural gas, the two systems are independent. The first recorded incident in 1976 in Kenosha, WI was an example of an incident of this type.

## Slide 18: Legacy Cross Bores

## Slide 19: Who Should Be Involved - Internal
Executive Management
Regulatory Affairs
Finance and Accounting
Public Relations
Training
Customer Service
Call Center Reps
Dispatch Operators
Field Operations
Engineering
Construction
General Utility Personnel

## Slide 20: Who Should Be Involved - External
Customers and Premise Owners
  Bill Inserts
  Direct Mailings
  Door Hangers
  Sewer Tags
  Outgoing Calls
Media
Municipal Gov’t and Sewer Owner/Oper.
One-Call System
Other Utilities
Contractors
Plumbers
Equipment Rental Owners
First Responders
Regulatory Agencies

## Slide 21: Public Awareness

## Slide 22: Cross Bore Public Awareness
Increase awareness of the hazards associated with gas/sewer conflicts
  Plumbing and sewer cleaning contractors
  Equipment rental companies
  Customers
Safety DVD
Bill inserts, advertisements, news media, online
Notes: The terms sewer or sewer system are used exclusively throughout this Guide to represent both the sanitary and storm sewer systems, as well as private septic systems.
The audience and topics covered by the How-To videos were:
Field personnel to avoid cross bores during new installations (2 minutes, 24 seconds);
Plumbers to inform them on how to investigate a clogged sewer (3 minutes, 6 seconds);
Homeowners/Do-it-yourselfers to inform them on the potential hazards of clearing a clogged sewer if the clog is outside the home/business (2 minutes, 12 seconds).

## Slide 23: Public Awareness Example

## Slide 24: Public Awareness – Door Hanger Examples

## Slide 25: Public Awareness – Sewer Tag Example

## Slide 26: Gas Operations
Awareness
Tailgate Briefings
Documentation

## Slide 27: What is a sewer cross-bore? The inadvertent placement of a gas main or service through a sewer line. Sewer cross-bores typically occur during trenchless construction. What can happen as a result of a sewer cross-bore? The sewer line may become blocked and need to be cleared with mechanical clearing tools. This may cause the gas line to be cut which could cause an explosion or fire. How can I avoid causing a sewer cross-bore? Excavating and locating sewer lines in advance of trenchless construction. What do I do if I discover a sewer cross-bore? Relocate the gas line and properly repair the sewer line. If you discover any other utility’s cross-bore, notify the building owner and the other utility. What do I do if I damage a sewer line? Ensure that it is repaired properly.
Sewer Cross-Bore Awareness for Gas Operations

## Slide 28
Laser-Compatible Paper - Tear Resistant, Water, Weather, Oil Proof – Ex. Revlar

## Slide 30
Laser-Compatible Paper - Tear Resistant, Water, Weather, Oil Proof – Ex. Revlar

## Slide 32: New/Replacement Documentation
If trenchless methods are used records should be kept of the decisions made by the crew or supervisor
Indicate the number of sewer laterals cleared of conflict
Use a sewer crossing verification summary on an “as-built” drawing or an electronic job record
Sign and date the document

## Slide 33: Sewer Crossing Verification

## Slide 34: Customer Service Representative or Dispatcher Quick Reference

## Slide 37: New Developments

## Slide 38: Acoustic Pipe Locator
Need/Benefits:
Locate gas distribution pipes with emphasize on detecting plastic pipes
  300,000 miles of plastic pipes without tracer wires in US alone
  500,000 to one million miles of plastic pipes without tracer wires in the world
  Tracer wires prone to damage/corrosion
    Increases miles of plastic pipes to be detected
  60%+ damage by third party
  Direct implications on operating cost and safety
Water and sewer lines
  Requirements:
  No special coupling liquids
  Use of same transducers for expected field conditions (dirt, grass, concrete, asphalt, etc.)
  Simple to operate and immediate results
  Pipe(s) display for locator/surveyor
  Cost-effective

## Slide 39: OTD Project Acoustic Pipe Locator
Technology licensed to Sensit Technologies
http://www.gasleaksensors.com/products/ultra-trac-acoustic-pipe-locator.html
Ultra-Trac APL
Display

## Slide 40: OTD Project Mechanical Spring - Cross Bore Detection
Goal - a tool that will detect a hit to sewer laterals during the HDD or mole installation of PE gas pipe.
The tool uses a low-cost, easy to use mechanical spring system attached to the HDD/mole head during drilling or to the PE pipe during pullback.
The spring system is activated inside the sewer pipe void; locating the lateral and providing a real-time alarm identifying a hit.

## Slide 41: OTD Project Mechanical Spring - Cross Bore Detection
Milestone Achieved: Completed design of Prototype C (4-inch diameter unit)
Next Step:
  Address new design options for the smaller diameter units (Prototype D)
  Complete IP-patent issue, contact HDD contractors
  Coordinate with contractor, run test at GTI
Expected Deliverable/Format:
  Refine design with HDD contractors
Contact:
  Michael Adamo …….

## Slide 42: OTD Project Mechanical Spring - Schematic Design

## Slide 43: OTD Project Mechanical Spring - Cross Bore Detection
Prototype A
(no electronics)
Prototype B
(direct signal to surface)
Prototype C
(Signal stored in device)

## Slide 44: OTD Project Obstacle Detection During HDD
Requirements:
  Detect obstacles in advance of HDD operations
  Sense both ahead of and adjacent to the drill bore
  Data acquisition and display must be rapid
    Simple display; Real time processing and display
Projects:
  Acoustic-based technology; Sensors on the ground
  GPR-based technology; Sensors incorporated in the drill head
Status:
  Acoustic technology provided detection of pipes about 20 ft. in front of drill head; Applicable for most soils; Requires improved accuracy/repeatability
  GPR technology detects pipes in close proximity; Good accuracy; Requires increase in pipe detection range; Issue on applicability in different soils
  Both projects running in parallel; Potential to combine efforts into one system; Very challenging projects
Notes: 44

## Slide 45: Sources of Additional Information